## Slide 1: SLAM-MR Simultaneous Localization and Mapping with Multiple Robots
Hammad Izhar and Thomas Kaminsky CS 2620 Final Presentation

## Slide 2: Simultaneous Localization and Mapping

## Slide 3: Simultaneous Localization and Mapping
Problem Setting:

## Slide 4: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)

## Slide 5: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)

## Slide 6: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)
RGB(D) Camera

## Slide 7: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)
RGB(D) Camera
LIDAR

## Slide 8: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)
RGB(D) Camera
LIDAR
RADAR/SONAR

## Slide 9: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)
  Odometry

## Slide 10: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)
  Odometry
Goal:

## Slide 11: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)
  Odometry
Goal:
  Maintain a ‘map’ of the environment and your ‘location’ within it

## Slide 12: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)
  Odometry
Goal:
  Maintain a ‘map’ of the environment and your ‘location’ within it
    Point Clouds
    Locations of interesting objects
    Walls

## Slide 13: Simultaneous Localization and Mapping
Problem Setting:
  Robot(s)
  Sensor(s)
  Odometry
Goal:
  Maintain a ‘map’ of the environment and your ‘location’ within it
    Point Clouds
    Locations of interesting objects
    Walls

## Slide 14: Multi-Robot SLAM
Benefits:

## Slide 15: Multi-Robot SLAM
Benefits:
  More sensors + parallelization

## Slide 16: Multi-Robot SLAM
Benefits:
  More sensors + parallelization
  Exploring with different capabilities

## Slide 17: Multi-Robot SLAM
Benefits:
  More sensors + parallelization
  Exploring with different capabilities
Challenges

## Slide 18: Multi-Robot SLAM
Benefits:
  More sensors + parallelization
  Exploring with different capabilities
Challenges
  Multiple Reference Frames

## Slide 19: Multi-Robot SLAM
Benefits:
  More sensors + parallelization
  Exploring with different capabilities
Challenges
  Multiple Reference Frames
  Communication costs

## Slide 20: Distributed PGO
Choudhary et al. (2017): Distributed Mapping with Privacy and Communication Constraints
Each robot does single-agent SLAM
During rendezvous with other robots:
  Neighbors exchange sensed relative poses
  Two rounds of distributed linear optimization (SOR) estimate:
    Global Rotation
    Global Translation
Point clouds can then be mapped to the common frame

## Slide 21: Distributed PGO
Choudhary et al. (2017): Distributed Mapping with Privacy and Communication Constraints
Each robot does single-agent SLAM
During rendezvous with other robots:
  Neighbors exchange sensed relative poses
  Two rounds of distributed linear optimization (SOR) estimate:
    Global Rotation
    Global Translation
Point clouds can then be mapped to the common frame

## Slide 22: Distributed PGO
Choudhary et al. (2017): Distributed Mapping with Privacy and Communication Constraints
Each robot does single-agent SLAM
During rendezvous with other robots:
  Neighbors exchange sensed relative poses
  Two rounds of distributed linear optimization (SOR) estimate:
    Global Rotation
    Global Translation
Point clouds can then be mapped to the common frame

## Slide 23: Distributed PGO
Choudhary et al. (2017): Distributed Mapping with Privacy and Communication Constraints
Each robot does single-agent SLAM
During rendezvous with other robots:
  Neighbors exchange sensed relative poses
  Two rounds of distributed linear optimization (SOR) estimate:
    Global Rotation
    Global Translation
Point clouds can then be mapped to the common frame

## Slide 24: Distributed PGO
Choudhary et al. (2017): Distributed Mapping with Privacy and Communication Constraints
Each robot does single-agent SLAM
During rendezvous with other robots:
  Neighbors exchange sensed relative poses
  Two rounds of distributed linear optimization (SOR) estimate:
    Global Rotation
    Global Translation
Point clouds can then be mapped to the common frame

## Slide 25: Distributed PGO
Choudhary et al. (2017): Distributed Mapping with Privacy and Communication Constraints
Each robot does single-agent SLAM
During rendezvous with other robots:
  Neighbors exchange sensed relative poses
  Two rounds of distributed linear optimization (SOR) estimate:
    Global Rotation
    Global Translation
Point clouds can then be mapped to the common frame

## Slide 26: Distributed PGO
Choudhary et al. (2017): Distributed Mapping with Privacy and Communication Constraints
Each robot does single-agent SLAM
During rendezvous with other robots:
  Neighbors exchange sensed relative poses
  Two rounds of distributed linear optimization (SOR) estimate:
    Global Rotation
    Global Translation
Point clouds can then be mapped to the common frame

## Slide 27: Distributed PGO
Choudhary et al. (2017): Distributed Mapping with Privacy and Communication Constraints
Each robot does single-agent SLAM
During rendezvous with other robots:
  Neighbors exchange sensed relative poses
  Two rounds of distributed linear optimization (SOR) estimate:
    Global Rotation
    Global Translation
Point clouds can then be mapped to the common frame

## Slide 28: Our System
Communication via ROS
Physics simulated using Gazebo and maps visualized in RViz
Right now, solution is in software
  Gazebo forces ‘physical realizability’ — all communication is performed via ROS topics
Should ease transition to hardware

## Slide 29: Our System
Communication via ROS
Physics simulated using Gazebo and maps visualized in RViz
Right now, solution is in software
  Gazebo forces ‘physical realizability’ — all communication is performed via ROS topics
Should ease transition to hardware

## Slide 30: Our System
Communication via ROS
Physics simulated using Gazebo and maps visualized in RViz
Right now, solution is in software
  Gazebo forces ‘physical realizability’ — all communication is performed via ROS topics
Should ease transition to hardware

## Slide 31: Crash Course in ROS Communications
Misnomer — not actually an operating system, but rather a distributed message passing service
Executed code units are referred to as ‘nodes’
Nodes can communicate with one another via ‘topics’
  Many-to-Many Publisher/Subscriber Model
Topics publish a single type of message
  Custom messages can be defined via an IDL, similar to gRPC messages

## Slide 32: Crash Course in ROS Communications
Misnomer — not actually an operating system, but rather a distributed message passing service
Executed code units are referred to as ‘nodes’
Nodes can communicate with one another via ‘topics’
  Many-to-Many Publisher/Subscriber Model
Topics publish a single type of message
  Custom messages can be defined via an IDL, similar to gRPC messages

## Slide 33: Crash Course in ROS Communications
Misnomer — not actually an operating system, but rather a distributed message passing service
Executed code units are referred to as ‘nodes’
Nodes can communicate with one another via ‘topics’
  Many-to-Many Publisher/Subscriber Model
Topics publish a single type of message
  Custom messages can be defined via an IDL, similar to gRPC messages

## Slide 34: Crash Course in ROS Communications
Misnomer — not actually an operating system, but rather a distributed message passing service
Executed code units are referred to as ‘nodes’
Nodes can communicate with one another via ‘topics’
  Many-to-Many Publisher/Subscriber Model
Topics publish a single type of message
  Custom messages can be defined via an IDL, similar to gRPC messages

## Slide 35: System Communication Setup
Every robot is associated with a node in its own namespace
Simulate UDP multicast – when a new robot spins up, it broadcasts itself to the entire team on the /team topic allowing other nodes to subscribe to its position estimates
Every thirty seconds from startup, a robot attempts to rendezvous with its nearby neighbors by broadcasting a custom `BeginRendezvous` message on the /rendezvous topic

## Slide 36: System Communication Setup
Every robot is associated with a node in its own namespace
Simulate UDP multicast – when a new robot spins up, it broadcasts itself to the entire team on the /team topic allowing other nodes to subscribe to its position estimates
Every thirty seconds from startup, a robot attempts to rendezvous with its nearby neighbors by broadcasting a custom `BeginRendezvous` message on the /rendezvous topic

## Slide 37: System Communication Setup
Every robot is associated with a node in its own namespace
Simulate UDP multicast – when a new robot spins up, it broadcasts itself to the entire team on the /team topic allowing other nodes to subscribe to its position estimates
Every thirty seconds from startup, a robot attempts to rendezvous with its nearby neighbors by broadcasting a custom BeginRendezvous message on the /rendezvous topic

## Slide 38: High Level Overview of Distributed PGO
A robot requires:

## Slide 39: High Level Overview of Distributed PGO
A robot requires:
  Sensed relative pose of their neighbors with respect to their current reference frame (/<neighbor_namespace>/pose)

## Slide 40: High Level Overview of Distributed PGO
A robot requires:
  Sensed relative pose of their neighbors with respect to their current reference frame (/<neighbor_namespace>/pose)
  Sensed relative pose of themselves with respect to their neighbors (/<neighbor_namespace>/local_pose_estimate)

## Slide 41: High Level Overview of Distributed PGO
A robot requires:
  Sensed relative pose of their neighbors with respect to their current reference frame (/<neighbor_namespace>/pose)
  Sensed relative pose of themselves with respect to their neighbors (/<neighbor_namespace>/local_pose_estimate)
  Their global pose estimate alongside those of their neighbors (/<neighbor_namespace>/global_pose_estimate)

## Slide 42: High Level Overview of Distributed PGO
A robot requires:
  Sensed relative pose of their neighbors with respect to their current reference frame (/<neighbor_namespace>/pose)
  Sensed relative pose of themselves with respect to their neighbors (/<neighbor_namespace>/local_pose_estimate)
  Their global pose estimate alongside those of their neighbors (/<neighbor_namespace>/global_pose_estimate)
An iteration consists of combining all of these values to update its own estimate of the global pose.

## Slide 43: High Level Overview of Distributed PGO
A robot requires:
  Sensed relative pose of their neighbors with respect to their current reference frame (/<neighbor_namespace>/pose)
  Sensed relative pose of themselves with respect to their neighbors (/<neighbor_namespace>/local_pose_estimate)
  Their global pose estimate alongside those of their neighbors (/<neighbor_namespace>/global_pose_estimate)
An iteration consists of combining all of these values to update its own estimate of the global pose.
This new value is then broadcast to a robot’s neighbors on its own global_pose_estimate topic

## Slide 44: Results: PGO – High Noise
10 Robots

## Slide 45: Results: PGO – High Noise
10 Robots
  Fully-connected communication graph

## Slide 46: Results: PGO – High Noise
10 Robots
  Fully-connected communication graph
Noise:
  Translation is Gaussian,
  Rotation is von-Mises,

## Slide 47: Results: PGO – High Noise
10 Robots
  Fully-connected communication graph
Noise:
  Translation is Gaussian,
  Rotation is von-Mises,
Optimization:
  100 Iterations for each component
  (for visualization)

## Slide 48: Results: PGO – High Noise
10 Robots
  Fully-connected communication graph
Noise:
  Translation is Gaussian,
  Rotation is von-Mises,
Optimization:
  100 Iterations for each component
  (for visualization)

## Slide 49: Results: PGO – High Noise
10 Robots
  Randomly-connected Erdős–Rényi,
Noise:
  Translation is Gaussian,
  Rotation is von-Mises,
Optimization:
  100 Iterations for each component
  (for visualization)

## Slide 50: Results: PGO – Low Noise
10 Robots
  Randomly-connected Erdős–Rényi,
Noise:
  Translation is Gaussian,
  Rotation is von-Mises,
Optimization:
  100 Iterations for each component
  (for visualization)

## Slide 51: Integrating Point Clouds
  We assign each robot a subset of a point cloud generated from a 2D scene
  Point clouds are relative to local robot frames
  Perform PGO as usual
  We visualize the integrated point cloud maps

## Slide 52: Point Cloud Results
  4 Robots
  Fully-connected communication graph

## Slide 53: Point Cloud Results
  10 Robots
  Fully-connected communication graph
  Medium noise

## Slide 54: Point Cloud Results
  10 Robots
  Fully-connected communication graph
  High noise

## Slide 55: Point Cloud Results
  10 Robots
  Sparse communication graph (ER .01)
  High noise

## Slide 56: Questions?